## Slide 1: Scalable Video Transmission for MobileTV
Farid Molazem
Network Systems Lab
Simon Fraser University

## Slide 2: Problem Statement
Broadcasting a number of scalable video streams from a base station to a large number of mobile receivers
  Bandwidth utilization
  Energy saving
  Quality of the transmitted video
We describe:
  Scalable Video Coding basics
  Formulation for our problem
  Results

## Slide 3: Scalable Video Coding
Scalable video coding
  Temporal scalability
  Spatial scalability
  Quality scalability
Temporal scalability
  Altering temporal resolution of a video
  Dropping random frames does not work
    Other frames might depend on them for motion compensation
  The frames must be encoded in hierarchical prediction structure

## Slide 4
GOP
GOP
0
4
3
5
2
7
6
8
1
12
11
13
10
15
14
16
9
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Four Temporal Layers
Non-Delay
Motion Prediction
Non-Dyadic
Temporal Layers

## Slide 5: Spatial Scalability
Images with different spatial resolutions
Each layer in the spatial scalable video stream improves the final image resolution

## Slide 6: Spatial Scalability
Inter-layer motion prediction
Inter-layer residual prediction
Inter-layer intra prediction

## Slide 7: Quality Scalability
Quality scalability could be considered as a special case of spatial scalability
Dividing the video into several quality layers: Coarse Grain Scalability (CGS)
In CGS, motion estimation is conducted in each spatial layer separately
  Switching between frames is only possible at I-frames
  The choice among different bitrates is limited to the number of layers

## Slide 8
Coarse Grain Scalability

## Slide 9: Quality Scalability
Alternatives for CGS:
  All quality levels in one spatial layer
Fine Grain Scalability
  Motion compensation is done at the lowest quality level of the reference picture

## Slide 10: Quality Scalability
FGS advantages:
  Encoder and decoder use the same quality level of the reference picture
  Bitrate scaling could be done at packet level
FGS disadvantage:
  Coding efficiency

## Slide 11: Quality Scalability
To improve motion prediction we can use the highest quality layer
The problem with this method is that it could cause drift
Drift

## Slide 12: Quality Scalability
Medium Grain Scalability
  A trade-off between Fine Grain Scalability and Coarse Grain Scalability
  Keeps drift at an acceptable level
  Motion prediction done in the enhancement layer with periodic updates at base layer

## Slide 13: Problem Formulation
Problem: Broadcasting S scalable video streams from a base station to a large number of mobile receivers over a wireless medium
Notation:
  There are S video streams
  Each frame video stream s has a base layer and MGS layers
  Each video stream has I frames
  Indicates the size of layer k of
  frame i of stream s
  Each stream is coded at F frame-per-second
Frame i of stream s
Base layer

## Slide 14: Problem Formulation
Energy Saving:
  The fraction of time the receivers can put their wireless receivers into sleep
  We use the average energy saving among all video streams
The average quality of all transmitted frames is shown by
  We use peak-signal-to-noise-ration (PSNR) as a quality metric

## Slide 15: Problem Formulation
Bandwidth Utilization
Energy Saving
Average Image Quality

## Slide 16: Problem Solution
buffer
buffer
buffer
Buffer being
drained
Buffer being
filled
Data
Size B
Size B/2
Size B/2
Image from
http://www.supgifts.com/images/cell%20phones/Cellphone652.jpg

## Slide 17: Problem Solution
Time window in which one
buffer is being drained and
another one being filled
The amount of data assigned to stream s in each time window should be the size of half a buffer
The length of time window should be equal to the playout time of the playing buffer
Stream s

## Slide 18: Problem Solution
The usefulness of a frame
s
s+1
s+2
Rescheduling window

## Slide 19: Adaptive windows
There is a trade-off between energy saving and bandwidth utilization
  We can constantly send small bursts of data for receivers, but the receiver circuits should be active all the time
Current time
Playout deadline of receivers

## Slide 20: Adaptive windows
Missed frames
New deadline

## Slide 21: Adaptive windows
Having a dynamic candidate set of streams
  Stream s becomes a candidate if α * B of the buffer size (B) gets drained
    Only schedule data for the streams in the candidate set
    If α is low, we tend to schedule data for the receivers early and when there is lower buffer space. This results in smaller bursts
    If α is higher, there will be more space in the receiver buffer and this could result into scheduling bigger bursts
Notes: hello

## Slide 22: Adaptive windows
Important parameters
  The buffer level
    is the number of frames sent for stream s
  The deadline
  The candidacy time

## Slide 23: Adaptive windows
At time t, we schedule a burst for a candidate stream s until either:
  Receiver buffer for stream s is full
  Time where is the stream with the closest candidacy time among all non-candidate streams
  Maximum burst size M
After scheduling a burst, whenever there is a missed deadline:
  We go back to time for which the decoding deadline of frames is not passed and set α= α/2
  We increase α after time t for each burst until it reaches to its initial value

## Slide 24: Video stream preparation
ffmpeg to convert mp4 files to yuv files
Joint Scalable Video Model (JSVM), the reference software for H.264/SVC
  BitstreamExtractorStatic
    To extract MGS layer information
    To create video streams with different quality layers
  PSNRStatic
    To extract PSNR value for each MGS layer of each frame

## Slide 25: Results

## Slide 26: Results

## Slide 27: Results

## Slide 28: Results

## Slide 29: Results

## Slide 30: Future Works
Analysis of the energy saving and bandwidth utilization based on adaptive parameter
Finding lower/higher bound for energy saving and bandwidth utilization based on adaptive parameter
Finding the updating formulation for the adaptive parameter that leads to the best results for energy consumption and bandwidth utilization

## Slide 31
Thanks You